## Slide 1
Image coordinates
eyeDataH + right on image (left on head)
CalculateEyeRotationQuaternion.m
eyeDataV
+ down
(0,0)
Torsion is top pole to right (pretty sure but need to double check)

## Slide 2: For quaternions
Pure rotations
Q2 = sin( rot around x / 2)
Q3 = sin( rot around y / 2)
Q4 = sin( rot around z / 2)

## Slide 3: CalculateEyeRotationQuaternion.m
Qt is rotation around axes from eye to camera
Q is supposed to be the quaternion that moves the gaze from the current position to the camera (or viceversa??)
Angle is the magnitude of the rotation of Q along an axis that is contained in the plane parallel to the camera.
ecc is the angle of that axis relative to the orientation of the camera
eyeCalibrationModelCenter
(y,z)
Angle

## Slide 4: CalculateEyeRotationQuaternion.m
Seems like q is being actually calculated in a left handed reference frame
q3 = -sin(angle)* sin(ecc/2);
should be q3 = sin(angle)* sin(ecc/2);
That however matches what openiris is doing.
// quaternion defining the rotation of the eyeball (ignoring torsion) just the center of the pupil
var yC = iris.Center.Y - eyeModel.Center.Y;
var xC = iris.Center.X - eyeModel.Center.X;
// First get the polar angle of the rotation. As the direction angle the eye moves from eye model center
// to iris center.
var angle = Math.Atan2(yC, xC);
// Then, get the eccentricity from the length of the vector in pixels to the angle that moves the eye that far
var ecc = Math.Asin(Math.Sqrt(yC * yC + xC * xC) / eyeModel.Radius);
// Finally get the quaternion that defines that rotation. This is a rotation without torsion in a reference frame perpendicular to the camera
var q = new Quaternions(Math.Cos(ecc / 2), -Math.Sin(angle) * Math.Sin(ecc / 2), Math.Cos(angle) * Math.Sin(ecc / 2), 0);

## Slide 5: When doing the rotation of the iris we build a 3D axis on the image to give volume to the eyeball. In this axis the z points out and the x and y axes are the ones from the image. So it becomes a left handed reference frame.
x + right on image (left on head)
y
+ down
(0,0)
Torsion is top pole to right (pretty sure but need to double check)
Z
+ out

## Slide 6: qEyePosInRef2Camera
Left-handed quaternion
(1,0,0,0) means looking at the camera with no torsion relative to the orientation of the camera

## Slide 7: camPosition
Left-handed quaternion
(1,0,0,0) eye pointing at the camera
Rotates the eye to look horizontal straight

## Slide 8: Data presentation in Arume
It is similar to the openiris:
  Downward is positive y and to the right is positive x